Bender Firmware Homing Routing

Logic:

The bender in order to begin a bend must have a starting point (0 position) reference because the bender maybe powered off from earlier sessions at an uncertain location. As such we propose this routing in order to find the starting reference. Additional 0-position for CW and CCW start positions maybe calculated based on diameter, but a fine tuning function should be included in order to adjust the CW and CCW 0 positions for out of tolerance diameter wire.

Firmware Spec.

The bender will have two limit switches for the maximum physical bend angle. The firmware upon start up (upon UI) interface button “Home” should move motors CW until hitting the end-stop, then the firmware should send the motor CCW with calculating the number of steps to the CCW maximum position (hitting the end stop). The firmware should then divide the number of steps in half to find the 0 position and move the bending pin to the true 0 position. (This regime should work until this point with the bending pin in the duck position). Then the feed should feed 10mm of wire, then based on a preset value for diameter. The routine should ask to verify (via UI) the CW 0 position off-set and the CCW 0 position off-set. The routine should then move 5 degrees CW, activate the pin (not in duck mode) and return to the theoretical angle based on diameter. If the pin touches the wire without bending the user via UI should hit OK. After this the CCW should be checked in a similar manner.
If the user hits OK, for both the CW 0 position and CCW 0 position the routing is finished.

If not the UI should prompt the user to go to “Fine Home Calibration”

Fine Home Calibration will first move the pin 10 degrees off of true 0 CW, activate the pin, and prompt the user to move the pin (via manual) till it is touching the wire. The firmware must calculate the number of steps away from 0 position and calculate the number of steps back (done in manual UI control). The user will then be offered to set CW zero position. The firmware will take the difference between the 10 degree steps and manually controlled back steps to know the CW zero position. The same regime will be done for CCW.